## Slide 1: ALTERNATING CURRENTS

## Slide 2: ac generator
A simple version of an alternator – a device that generates an emf
The magnetic field is uniform and constant. At time t = 0,
is an angular velocity
where f is frequency
where T is a period
The output v(t) = V0 sin 𝜔t of an ac generator.
Symbol used to represent an ac voltage source in a circuit diagram.

## Slide 3: Resistor in an ac circuit
Current and voltage are
in phase with each other.
A resistor connected across an ac voltage source.
The current iR(t) through the resistor and the voltage vR(t) across the resistor. The two quantities are in phase.

## Slide 4: rms current
What is the average current in a resistor?
Root-mean-square current
For the resistor in an ac circuit
“120-V ac” means the rms voltage, not the maximum, which is 170 V!
rms current is a dc current that would produce the same power output as the actual ac circuit!

## Slide 5: Inductor in an ac circuit

## Slide 6: Inductor in an ac circuit, continued
Current lags behind the voltage by 90 degrees.
or
where (inductive reactance)
Note: units of the inductive reactance are Ohms!

## Slide 7: An inductor in an ac circuit example
Suppose you want the current amplitude in a pure inductor in a radio receiver to be 250 mA when the voltage amplitude is 3.60 V at a frequency of 1.60 MHz (corresponding to the upper end of the AM broadcast band). What inductive reactance is needed? What inductance? If the voltage amplitude is kept constant, what will be the current amplitude through the inductor at 16.0 Mhz?

## Slide 8: Capacitor in an ac circuit
Where
is capacitive reactance

## Slide 9: Capacitance in an ac circuit
Current leads the voltage by 90 degrees
Remember ELI the ICE man mnemonics!

## Slide 10: Example: the capacitive reactance
What is the capacitive reactance of a
capacitor at a 100 H z audio frequency and at a 100 M H z F M-radio frequency?

## Slide 11: Comparing ac Circuit Elements
The graph shows how the resistance of a resistor and the reactances of an inductor and a capacitor vary with angular frequency
Resistance R is independent of frequency.
If corresponding to a dc circuit, there is no current through a capacitor because
In the limit the current through
an inductor becomes vanishingly small.

## Slide 12: Phasors
Phasor is a vector rotating around the origin of a coordinate system
Length of the phasor corresponds to a maximum value of a current (or voltage)
Projection of a phasor onto vertical axis at
a moment t equals the instantaneous value of
a current (voltage)

## Slide 13: Phasor diagram for the resistor
The phasor diagram representing the current through the resistor
The phasor diagram representing both iR(t) and vR(t) .

## Slide 14: Phasor diagram for an Inductor
The phasor diagram for the inductor. The current phasor lags the voltage phasor by 𝜋/2 rad as they both rotate with the same angular frequency.

## Slide 15: Phasor diagram for a capacitor
The phasor diagram for the capacitor. The current phasor leads the voltage phasor by 𝜋/2 rad as they both rotate with the same angular frequency.

## Slide 16: The L-R-C series circuit
Many ac circuits used in practical applications involve resistance, capacitance, and inductance
Can be analyzed with phasor diagram

## Slide 17: Phasor diagrams for the L-R-C series circuit
The phasor diagram for the circuit.

## Slide 18: The L-R-C series circuit, continued
The resultant of the phasors for vL(t) , vC(t), and vR(t) is equal to the phasor for v(t) = V0 sin ωt. The i(t) phasor (not shown) is aligned with the vR(t) phasor.